Test Scenario:

The test is performed in the institute’s hallway, cluttered with obstacles. In this setup the robot is planned to move 11 meters in the hallway, and three obstacles with different dimension are defined.

Obstacle 1: 13 cm*21 cm
Obstacle 2: 15 cm*24.5 cm
Obstacle 3: 11.5 cm* 10 cm

Respective position for these obstacle on pathway are: 180 cm,600 cm and 800 cm

Neglect the open space of 335 cm which is going to expand when AV moves approx 700cm.

Test Equipment:

- Laser sensor connected with 24 V battery
- A cart with wheels
- Computer
-Three obstacles with above dimension
-DC Motor

Procedure:

- First of connect the respective apparatus with power supply and embedded on cart such that the face
   of Laser is in front direction and no object is kept in protective field area. Laser glass should be clean
   properly that no glares are found while testing.

- Put the cart on the center of pathway such that at least 250 cm of distance is left between boundary
   and AV.

- Make sure AV drives straight on dedicated path.

-While AV moves in forward direction. Laser will sense the object and AV will reduced speed and it
  will stop 40 cm before the obstacle.

-It will take immediate right or left turn bypass the obstacle and again starts into a straight path.

-Same procedure is applicable for predefined NO GO areas.

- Emergency stop button is used to stop vehicle at finish line as well as some moving obstacle is
   detected during run operation.

-Be Cautious of battery level. If it less than 40% it is not advisable to test.

-If turning radius of AV is inadequate, it is advisable to take AV in backward direction check the

- To make observations, the main parameters which should be focus are deviation of cart, obstacle detection and avoidance.